## Slide 2: National Traffic System Handling Formal Messages
Emergency Communications Workshop
2

## Slide 3: Radiogram Format
3/5/2011
Emergency Communications Workshop
3

## Slide 4: Formal Written vs. Tactical Messages
Emergency Communications Workshop
4
Most emergency traffic is tactical
Formal written traffic is important for:
  A record of what has happened —
  Ability to track
  Use when relays are required in order to keep messages intact
  Use of radiogram unless other formats such as ICS-213 or agency formats are required
Notes: Organization, sending ops here or there, different frequencies

## Slide 5: Radiogram Preamble: Precedence
Emergency Communications Workshop
5
Precedence is R, W, P or EMERGENCY
  Emergency [Never Abbreviated]
    life and death urgency, officially designated
  P - Priority
    other official or urgent / time sensitive
  W - Health and Welfare
    outgoing: advisory all is well etc.
    incoming: inquiry as to H&W of someone.
  R - Routine

## Slide 6: Radiogram Contents Preamble
Emergency Communications Workshop
6
Number (1,…)
Precedence (R, W, P or EMERGENCY)
Handling Instructions (HXA…HXG)
Station of Origin (your call sign if you originated it)
Check (count of number of words/groups in body text)
Place of Origin (where sent from)
Date (Time/Date) Filed, Time zone

## Slide 7: Radiogram Preamble: Handling Instructions
Emergency Communications Workshop
7
Handling Instructions (optional,)
  HXA(#)—Collect miles
  HXB#—Cancel hours
  HXC—Report TOD
  HXD—Trace
  HXE—get reply
  HXF#—Hold until #date
  HXG—Free delivery only

## Slide 8: Radiogram Contents The Rest
Emergency Communications Workshop
8
Address as complete as possible
Text (Body)
  Separate from Address with break (BT)
  Limit to 25 words or less, if possible.
  Use X for punctuation between sentences but not at end
Signature
  Separate from Text with break (BT)
  Name
    Phone number suggested for reply addressing
Operators Notes (Optional)
  Separate from Signature with break (BT)

## Slide 9
This is how it starts.
Just write it down.
This what this session
sounded like on HF.

## Slide 10
ARRL Numbered Radiograms
FORTY SEVEN Reference your message number _____ to _____ delivered on _____ at _____ UTC.

## Slide 11
Good day Robert KC1KVY,
Ko4dn has relayed this message by radio from Tallahassee, Fl
to you.
Message:
Referencing your message number 3124 was delivered on March 27 2234 UTC
via email.
73,
Kris ko4dn
For the Marion County Traffic Net
For the Florida Phone Traffic Net
Gray Moffett KC3DWY
Assistant Emergency Coordinator
Marion County Amateur Radio Emergency Service
www.aresmcfl.org
Now I want to turn this Numbered Message into a meaningful script

## Slide 12: Pro-Words
Figure – single numeral follows
Figures – several numerals follow
Letter Group – usually an abbreviation (EOC)
Mixed Group – letters and numerals (12A)
Amateur Call – special type of mixed group
I Spell – phonetic spelling follows
I Say Again – repeat of previous word
Emergency Communications Workshop
12

## Slide 13: Pro-Words (2)
Correction – I’m going to correct something
End – end of message
More – additional message(s) follow
No more – no additional messages
Say Again – request from recipient to repeat
  Word after
  Word before
  All after
  All before
  Between
13
Emergency Communications Workshop

## Slide 14: If Check Doesn’t Match
Clarify special items, e.g., email address is 5 words
Read message at reading speed stopping after every 5 words so recipients can identify where count is off or read every fifth word
Note discrepancy in count in optional Operator’s Notes
Emergency Communications Workshop
14

## Slide 15: Radiogram: “Properly Serviced”
Emergency Communications Workshop
15
For a message to be “properly serviced” and thus traceable, record how it traveled. This may be in your traffic log or on an actual Radiogram form for each message.
Received from another station
  For all messages except those originated, record
  Received From: Station, date, time received from.
If relaying to another station
  Sent To: Station, date, time relayed
If delivering hard-copy to addressee,
  Received At: Your call, phone, name address
Send Reply to sender or Service message to Originator
Notes: Slide 6

## Slide 16: IMPORTANT
Goal is to get the message through intact!
From the ARRL NTS Methods and Practices Guidelines – MPG. Do what the trained receiving operator expects and confusion and errors will be minimized
Emergency Communications Workshop
16

## Slide 17: NTS Net Schedule
17
NTS Net Schedule and also where to send NTS messages via Packet.
Check out the NTS web site at ema.arrl.org/national-traffic-system/ for updates on NTS and the net schedule.
Net | Time | Frequency | Mode | Net Manager
EM2MN | 8:00 PM | 145.23- PL: 88.5 | FM | Peter –KC1HHO
CM2MN | 9:00 PM | 146.97- PL: 114.8 | FM | John-KK1X
HHTN | 10:00 PM SuMWF | MMRA System PL: 146.2 | FM | Joe-W1HAI
CITN | 7:30 PM TuThFSa | 147.375- PL: 110.9 | FM | Mark-AC7RB
MARIPN | 5:00 PM M-Sa | 3.978 MHz | LSB | Ralph-N1LAH
MARI | 7:00 PM | 3.565 MHz | CW | Marcia-KW1U
MARISN | 8:30 PM MTuFSa | 3.598 MHz | CW | Rob-K2MZ

## Slide 18: Traffic Nets Cont.
Region Nets
  FRN 3.950 Khz SSB 2:45 & 4:15 PM (during Daylight Savings Time)
  1RN 3.598 Khz CW 7:45 & 9:30 PM
  Digital
  KW1U MBO 24/7 VHF Packet 145.090 Mhz & HF Pactor (scanning multiple frequencies. See kw1u@arrl.net for further information)
  Winlink via kw1u@winlink.org

## Slide 19: Resources
ema.arrl.org/national-traffic-system/
Check NTS Resources under Quick Links
Includes fillable Radiogram form, ITU Phonetics, etc.
winlink.org
arrl.org Methods and Practices Guidelines (MPG)
From the ARRL NTS Methods and Practices Guidelines MPG - Do what the trained receiving operator expects and confusion and errors will be minimized